## Slide 1: WJEC GCSE Digital Technology
Unit 1:
The digital world
DT10: Network hardware

## Slide 2
Knowledge retrieval
How many points can you score?
Which type of network covers a small geographical area? (1 point) | Which type of network gives devices equal responsibility? (1 point) | Name THREE methods of interaction (2 points)
Name TWO cloud storage providers. (3 points) | Name TWO types of optical storage (4 points) | Name TWO types of magnetic storage (5 points)
Name TWO types of solid-state storage (5 points | Name TWO types of digital graphic (6 points) | Name three characteristics of the CPU that can impact performance (7 points)
How is image resolution measured? (8 points) | How many bits are required to store 4 colours in one pixel? (9 points) | Name THREE image file formats (10 points)

## Slide 3
Knowledge retrieval
How many points can you score?
Which type of network covers a small geographical area? (1 point) LAN (Local Area Network) | Which type of network gives devices equal responsibility? (1 point) Peer-to-Peer network | Name THREE methods of interaction (2 points) Touch, Speech, Gesture, Traditional, Virtual Reality, Augmented Reality.
Name TWO cloud storage providers(3 points) Google Drive, Dropbox, OneDrive (Other examples accepted) | Name TWO types of optical storage (4 points) CD, DVD, Blu-ray | Name TWO types of magnetic storage (5 points) Magnetic tape, Floppy disk, Hard drive
Name TWO types of solid-state storage (5 points SD Card, Solid-state drive, USB Flash Drive | Name TWO types of digital graphic (6 points) Vector and Bitmap | Name three characteristics of the CPU that can impact performance (7 points) Clock speed, Cores, Cache size
How is image resolution measured? (8 points) Per inch/mm/unit area | How many bits are required to store 4 colours in one pixel? (9 points) 2 Bits | Name THREE image file formats (10 points) PNG, JPG, TIFF, RAW, PSD, BMP

## Slide 4
Exam prep!
The revision starts here!!
Describe what is meant by a client-server network
……………………………………………………………………………
……………………………………………………………………………
……………………………………………………………………………
[2]
Describe means to…
Give a detailed account or picture of a situation, event, pattern or process.
In this question you need two key points such as:
How is your data stored? Where does it go? (1 mark)
How are you connected to the network? (1 mark)
What does a client-server network allow you to do? (1 mark)

## Slide 5
Exam prep!
The revision starts here!!
1 mark per bullet:
All devices are connected to a central server.
The central server receives and processes requests from ‘clients’.
The server stores user account details and files.
Sharing of resources (by example)
Describe what is meant by a client-server network.
All devices are connected to a centralised location known as the server. This allows users of the network to share resources such as use of software and printing.
[2]



## Slide 6
Concept map
Types of networks
LAN
WAN
Preferred topology
Star
Preferred topology
Mesh
Network hardware:
Network models:
Peer-to-peer
Client-server
Switch
Router
Hub
NIC
Server
Wireless Access Point
Transmission media:
Ethernet
Fibre optic cable
Telephone lines

## Slide 7: Lesson Objectives:
Curricular goal:
The hardware needed to connect stand-alone computers into a Local Area Network: Wireless access points, Routers, Switches, Bridge and Gateway.
Identify different types of network hardware and the tasks they perform.
Recommend and justify network hardware required to set up the network infrastructure within a shopping centre.
Lesson components:

## Slide 8
Key terms
Important terms:
Hub
Bandwidth
Ports
Data packets
Data collisions
MAC address
IP address
Switch
Router
Wireless Access Point
Network Interface Controller
Key words | 
Hub | It does not to filter any data so when data arrives, it’s sent to all the other devices on that network.
Bandwidth | The amount of data that can be transmitted in a given period of time
Ports | A physical connection on a computer or another electronic device
Data packets | A unit of data made into a single package that travels along a given network path
Data collisions | The result of simultaneous data packet transmission between two or more network domain devices or nodes
MAC address | Used to uniquely identify a device connected to a network.
IP address | A numerical label assigned to each device connected to a computer network
Switch | When data is sent to a switch, it’s only redirected to the intended destination.
Router | To connect different networks together.
Wireless Access Point | These are used to connect cabled networks.
Network Interface Controller | All computers need one to connect to a network.

## Slide 9
Hub
Every machine at the start is a standalone computer which means it’s not connected together in any way with other devices. In order to convert it from a standalone to a networked computer, it requires hardware.
Video
Click here
Question:
What is the purpose of the hub? What connections are required to connect devices to the hub? What does it mean when the hub has ‘no intelligence’? What problems to the network could using a hub cause?
Answer:
Connect all devices together on an internal network. Ethernet cable It does not have the ability to filter data so it goes to the intended recipient, the data is sent to all devices connected to the network. Security issues and creates unnecessary traffic which increases the risk of data collisions and consumes a lot of bandwidth.
Notes: First 1.39 of video for Hub

## Slide 10
Switch
As time went on, hubs became obsolete due to it’s impractical nature. As networks were continually upscaling, there was a requirement to change the way data packets are transmitted across an internal network and this where the switch came in.
Video
Click here
Question:
How is a switch similar to the hub? What does it mean when the switch has ‘intelligence’? Why is a switch preferred to a hub?
Answer:
It also connects all devices together on an internal network using ethernet cables to connect devices to an internal network. The switch is able to learn the MAC addresses of each device connected to the network which means the data packets can be re-directed to it’s intended location only. Reduces security issues and reduces unnecessary traffic which decreases the risk of data collisions and consumes less bandwidth.
Notes: Up to 3.15 on the video for Switch

## Slide 11
Router
Hubs and Switches are great for setting up internal networks such as a LAN. But the internet is part of a WAN (Wide Area Network) and in order for internal networks to connect to the internet, it needed a router. Just like how our home networks need a router to connect to the internet.
Video
Click here
Question:
What can the router do that a hub or switch cannot? What is the purpose of the router? What is the key difference between a hub/switch and router?
Answer:
A router can exchange data outside of their own network (such as the internet) and it has the ability to read IP addresses which hubs and switches cannot do. To transmit data from one network to another based on their IP address. So when the router receives that data, it is then re-directed to it’s intended location. Hubs and Switches are used to create networks whereas Routers are used to connect networks.
Notes: Rest of the video

## Slide 12
Wireless Access Point
The ability to connect to a network wirelessly does have it’s benefits. But one of the main drawbacks is the coverage, it can only cover a certain range and this is where Wireless Access Points are useful.
Video
Click here
Question:
How can devices connect to this home network? How does a Wireless Access Point work? Who would typically use a Wireless Access Point? What is one of the main reasons for using this? (Following on from Q3) Why couldn’t they just install extra routers?
Answer:
They can connect wirelessly by using Wi-Fi signal or they can connect physically with an ethernet cable because the router as a built-in switch. It relays data between a wired network and wireless devices. Medium to large organisations to provide greater coverage. Because it can be managed by one single router. It would become to difficult to manage because the network technician would need to configure all routers if changes needed to be made.
Notes: Watch video for in-class discussion.
Beyond the spec but good for context.

## Slide 13
Transmission media
In order to transmit data over a network, they need to be connected by some form of cabling and this can vary depending on the situation. One popular method used today is fibre optic cabling.
Video
Click here
Question:
Why is fibre optic cabling so popular? How do fibre optic cables transmit data? What benefits does it have over traditional copper cables? Use the internet to find other different types of transmission media.
Answer:
Because it provides the fastest internet speeds. Download and upload speed of 1,000 Mbps. Uses light to send data. The core part of the cable is a continuous strand of super thin glass that is roughly the same size as a human hair. It can travel much longer distances. This is because signals in a copper cable can be affected by electromagnetic interference. Possible answers: Ethernet, Satellite, Telephone lines, Coaxial cables
Notes: Watch video from 5:15 for in-class discussion.
Then complete both worksheets
Beyond the spec but good for context.

## Slide 14
Self-checker tool
How confident are you that know what is meant by the following terms:
The hardware needed to connect stand-alone computers into a Local Area Network:
  Wireless access points
  Routers
  Switches
  Bridge
  Gateway
Question:
Complete the multiple-choice quiz provided by your teacher to check understanding.
Notes: This is the quiz template for teachers to share with their students:
https://forms.office.com/Pages/ShareFormPage.aspx?id=cdJyXzS9Y0yZF8UZZlqALiw7DWJu831Jg5qPZF4a9X9UQ1hQVlpWR0UzQzFPV1hFMVBSWVNCWExKWS4u&sharetoken=G1J66t724y1TgfOqcpeO