## Slide 1: WJEC GCSE Digital Technology
Unit 1:
The digital world
DT10:
Network hardware

## Slide 2
Starter
Name one pro and one con for each type of connection below.
Name one pro: ……………………………………………………………………………… | Name one pro: ……………………………………………………………………………… | Name one pro: ………………………………………………………………………………
Name one con: ……………………………………………………………………………… | Name one con: ……………………………………………………………………………… | Name one con: ………………………………………………………………………………
Notes: Ethernet cable source: https://www.pxfuel.com/en/search?q=Ethernet
Wi-Fi source: https://www.needpix.com/photo/626914/wifi-wireless-device-wi-fi-free-pictures-free-photos-free-images-royalty-free
Fibre optic cable source: https://www.pikrepo.com/fmium/blue-and-yellow-fiber-optic-cables

## Slide 3
Starter
Name one pro and one con for each type of connection below.
Name one pro: Better security Fast transfer speeds, compared to Wi-Fi | Name one pro: Great mobility, not restricted by a wire. Cost effective – only need router. | Name one pro: Faster transfer speeds Travel long distance
Name one con: Less mobile, restricted by length of cable. Installation could prove expensive. | Name one con: Has a limited range Subject to interference. | Name one con: Expensive
Notes: Ethernet cable source: https://www.pxfuel.com/en/search?q=Ethernet
Wi-Fi source: https://www.needpix.com/photo/626914/wifi-wireless-device-wi-fi-free-pictures-free-photos-free-images-royalty-free
Fibre optic cable source: https://www.pikrepo.com/fmium/blue-and-yellow-fiber-optic-cables

## Slide 4: Lesson Objectives:
Curricular goal:
A network is two or more computers (or other electronic devices) that are connected together, usually by cables or Wi-Fi.
Understand the purpose of a Network Interface Controller (NIC)
Identify differences between an IP address and a MAC address.
Identify the characteristics of different types of network hardware: Router, Hub, Switch and Wireless Access Point.
Consolidate your knowledge and understanding by answering exam-style questions.
Lesson components:

## Slide 5
Keyword Bank
Try and use as many keywords from today’s keyword bank.
Data | Networks | Signals | Filter | Format
Forward | Receive | Addresses | Connect | Destination
Packets | Inspect | Devices | Identify | Intelligent
Unique | Internal | External | MAC | IP

## Slide 6
New information: Network Interface Controller
All computers need a Network Interface Controller (NIC) to connect to a network.
Modern computers all come with a built in NIC – but this wasn’t the case many years ago.
Each NIC will be assigned unique identification number which cannot be changed or copied.
This unique form of identification is called a MAC address.
MAC stands for Media Access Control.
It’s programmed into the NIC to ensure the data is directed to it’s intended location.
More facts about MAC Addresses:
MAC addresses can't be changed / every device has a fixed MAC address
MAC addresses are 6 bytes long.
MAC addresses are normally written in Hex.
MAC addresses are configured in hardware.
MAC addresses are only used within the LAN
Discussion:
Look at the facts provided about MAC addresses. How are IP addresses different?
Notes: NIC Source: https://pxhere.com/en/photo/1387078
Discussion icon source: https://thenounproject.com/term/group-discussion/961250/

## Slide 7
New information: IP Addresses v MAC Addresses
MAC Address | IP Address
MAC addresses can't be changed / every device has a fixed MC address | IP addresses can be changed / are allocated as needed
MAC addresses are 6 bytes long. | IP(v4) addresses are 4 bytes long
MAC addresses are normally written in Hex. | IP(v4) addresses are normally written in denary
MAC addresses are configured in hardware. | IP addresses are configured by software
MAC addresses are only used within the LAN | IP addresses are used for routing across a WAN / internet
E4-BC-E9-8D-45-7A
172.16.254.1

## Slide 8
Network hardware:
Watch the video provided and match up the statements with the correct piece of hardware by ticking the boxes.
Statement | Hub | Wireless Access Point | Router | Switch
To connect all of your network devices together on an internal network. |  |  |  | 
Addresses of the devices that are connected to it and it stores these in physical addresses called MAC addresses. |  |  |  | 
Data packets are only directed to the intended destination port because the device is intelligent. |  |  |  | 
Used to connect networks. |  |  |  | 
These are used to connect cabled networks. They convert data received through cables into wireless signals. |  |  |  | 
Inspects the data’s IP address. |  |  |  | 
Using this will create unnecessary traffic and wastes bandwidth. |  |  |  | 
Notes: https://www.youtube.com/watch?v=1z0ULvg_pW8&t=2s
Video for WAP:
https://www.youtube.com/watch?v=OxiY4yf6GGg&t=84s

## Slide 9
Network hardware:
Watch the video provided and match up the statements with the correct piece of hardware by ticking the boxes.
Statement | Hub | Wireless Access Point | Router | Switch
To connect all of your network devices together on an internal network. |  |  |  | 
Addresses of the devices that are connected to it and it stores these in physical addresses called MAC addresses. |  |  |  | 
Data packets are only directed to the intended destination port because the device is intelligent. |  |  |  | 
Used to connect networks. |  |  |  | 
These are used to connect cabled networks. They convert data received through cables into wireless signals. |  |  |  | 
Inspects the data’s IP address. |  |  |  | 
Using this will create unnecessary traffic and wastes bandwidth. |  |  |  | 
Notes: https://www.youtube.com/watch?v=1z0ULvg_pW8&t=2s
Video for WAP:
https://www.youtube.com/watch?v=OxiY4yf6GGg&t=84s

## Slide 10
1-2-3-4-5!!!
Describe the purpose of a Gateway (1 mark)
…………………………………………………………………………………………………………………………………………………………
Describe the purpose of a Bridge (2 marks)
………………………………………………………………………………………………………………………………………………………………………………………………………………………………………
Describe the purpose of a Hub. (3 marks)
……………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………
Describe the purpose of a Router. (4 marks)
…………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………
Describe the purpose of a Switch. (5 marks)
…………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………
Notes: The purpose of this task is to help students build descriptive answers through scaffolding.

## Slide 11
1-2-3-4-5!!!
Describe the purpose of a Gateway (1 mark)
A gateway joins together two networks that use
different base protocols
Describe the purpose of a Bridge (2 marks)
A bridge joins together two networks that use the
same base protocols, e.g. links LAN to LAN.
Describe the purpose of a Hub. (3 marks)
To connect all the devices together on a network. It’s designed not to filter any data so when data arrives, it’s sent to all the other devices on that network.
Describe the purpose of a Router. (4 marks)
To connect different networks together. It works by receiving data and inspecting it’s IP address. Once it determines who the data is intended for, it is then forwarded to the correct network.
Describe the purpose of a Switch. (5 marks)
To connect all the devices together on a network. It’s an intelligent device which has the ability to store the addresses of the devices connected to it. The addresses they store are called MAC addresses, which is a way of uniquely identifying a device on a network. So when data is sent to a switch, it’s only redirected to the intended destination.