## Slide 1
DT3 – Measuring and storing data
Text file size:
Why do computers use bits?
Binary is a number system that only uses two digits: 1 and 0. All information that is processed by a computer is in the form of a sequence of 1s and 0s. Therefore, all data that we want a computer to process needs to be converted into binary. These digits 1 and 0 are often referred to as bits.
Image file size:
Sound file size:
Formula:
text file size = bits per character x number of characters
Formula:
image file size = colour depth x image height (px) x image width (px)
Formula:
sound file size = sample rate x duration (s) x bit depth
Units of data storage:
Order (Smallest to largest) | Unit | Equivalent
1 | Bit | 0 or 1
2 | Nibble | 4 bits
3 | Byte | 8 bits
4 | KB | 1,000 Bytes
5 | MB | 1,000 KB
6 | GB | 1,000 MB
7 | TB | 1,000 GB
8 | PB | 1,000 TB
Exam tip:
Use of 1,024 for conversions and calculations would be acceptable. Allowance for metadata in calculations may be used
Worked example:
Sample rate = 3 Duration = 1 minute 30 seconds Bit depth = 2 3 x 90 x 2 = 540 bits
Worked example:
An image that is 400 x 400 with a colour depth of 4 bits. (400 x 400) x 4 = 640000 bits 640000/8 = 80,000 bytes
Worked example
Document that consists of 56 characters. 50 x 8 = 400 and 6 x 8 = 48 (400 + 48 = 448 bits)